## Slide 1
Core Compute Engine Energy Comparison
Isolating Architecture from System: All at 7nm, No External Memory
Three Distinct Modeling Domains:
1. Core Compute Engine
Scalar ALU, SIMD ALU, SM/CU, Systolic Array, PE Array + their local register files/buffers NOT workload-dependent. Determined by architecture.
THIS DECK
2. On-Chip Memory
L1/L2/L3 caches (CPU) Shared Memory + L2 (GPU) Unified Buffer (TPU) EDDO Scratchpads (KPU) Workload-dependent. Data reuse pattern matters.
Future deck
3. Memory Controller + I/O
NoC / Crossbar to mem ctrl DDR/LPDDR/GDDR/HBM PHY External DRAM access System-dependent. Packaging + memory technology.
Memory Tech deck
Core Compute Engines Compared (all at 7nm TSMC N7):
CPU
Scalar ALU + RF SIMD ALU (AVX-512) + VRF Granularity: 1 or 16 ops/instr
GPU SM
32 CUDA Cores + 1 TensorCore + 16K Register Bank + Warp Sched + Scoreboard + Operand Collector + Crossbar Granularity: 32 or 64 ops/instr x4 partitions = 1 SM
TPU Tile
Input Buffer (SRAM) + 128x128 Systolic Array + Accumulators Granularity: 16,384 MACs/cycle Weight-stationary only
KPU Tile
Input Buffer (EDDO L1) + 16x16 PE Array + SURE Network Granularity: 256 MACs/cycle A/B/C-stationary (any schedule)

## Slide 2
CPU Core Compute Engine: Scalar + SIMD ALU
Scalar Path (1 op per instruction)
I-Cache Read
0.540 pJ
Instruction Decode
0.288 pJ
RF Read (src1)
1.013 pJ
RF Read (src2)
1.013 pJ
Scalar ALU (FP32 FMA)
1.800 pJ
RF Write (result)
1.215 pJ
Total: 2 * (0.540 + 0.288) + 2 * 1.013 + 1.800 + 1.215
= 9.936 pJ/op | Compute eff: 18.1%
SIMD Path (AVX-512: 16 ops per instruction)
I-Cache Read (1 instr)
0.540 / 16 = 0.034 pJ/op
Decode (1 instr)
0.288 / 16 = 0.018 pJ/op
VRF Read src1 (1 vec reg)
1.013 / 16 = 0.063 pJ/op
VRF Read src2 (1 vec reg)
1.013 / 16 = 0.063 pJ/op
SIMD ALU x16 (FP32 FMA)
16 x 1.800 / 16 = 1.800 pJ/op
VRF Write (1 vec reg)
1.215 / 16 = 0.076 pJ/op
(0.540 + 0.288 + 2*1.013 + 1.215) / 16 + 1.800
= 2.309 pJ/op | Compute eff: 78.0% | 4.3x better than scalar
CPU Energy Equation: E_cpu = (E_ifetch + E_decode + 2*E_rf_read + E_rf_write) / SIMD_width + E_alu
SIMD amortizes the instruction overhead over 16 lanes. The ALU energy (1.800 pJ) is identical.
Wider SIMD = higher efficiency, but the instruction pipeline ALWAYS exists. Every op needs an instruction.
Granularity: 1 core = 1 scalar ALU + 1 SIMD ALU | Multi-core: N cores share L3 | Each core has private L1i/L1d + L2

## Slide 3
GPU SM: SIMT Engine + TensorCores + 64K Register File
One SM partition (x4 per SM): the indivisible GPU compute block
SM Partition (1 of 4)
Warp Scheduler
0.875 pJ/instr
Scoreboard (RAW/WAW/WAR)
0.525 pJ/instr
Register Addr Gen (x3)
1.050 pJ/instr
Operand Collector
1.400 pJ (CUDA) / 0.875 pJ (TC)
Bank Arbitration (32 banks)
0.525 pJ (CUDA) / 0.350 pJ (TC)
Register File Bank (16K regs)
0.281 pJ x 2 reads (CUDA)
Crossbar (32-wide)
0.700 pJ (CUDA) / 0.525 pJ (TC)
32 CUDA Cores / 1 TensorCore
1.530 pJ/op (both paths)
Result Route + RF Write
0.525 + 0.338 pJ (CUDA)
Energy Equations (per MAC, amortized over warp)
CUDA Core Path (amortized over 32 threads):
E_cuda = (E_sched + E_score + E_addr + E_coll + E_arb + E_rf + E_xbar + E_wb) / 32 + E_alu
= (0.875+0.525+1.05+1.40+0.525+0.562+0.70+0.863) / 32 + 1.530
= 0.203 (overhead) + 1.530 (ALU) = 1.733 pJ/op | Eff: 88.3%
TensorCore Path (amortized over 64 MACs per MMA):
E_tc = (E_sched + E_score + E_addr + E_coll + E_arb + E_rf + E_xbar + E_wb) / 64 + E_alu
= (0.875+0.525+0.788+0.875+0.35+0.90+0.525+0.978) / 64 + 1.530
= 0.075 (overhead) + 1.530 (ALU) = 1.605 pJ/op | Eff: 95.3%
The Critical Point: Per-MAC vs Per-SM
Per-MAC overhead looks small (0.07-0.20 pJ) because it's amortized
over 32-64 MACs. But the SM has 4 partitions, each with:
* 16K registers (64 KB SRAM) -- always powered
* Warp scheduler + scoreboard -- tracking 16 warps
* Operand collector -- continuous buffering
* Crossbar -- always ready for next warp switch
This infrastructure exists for ALL 2048 resident threads.
Static power of 256 KB RF is NOT in the per-instruction model.
Granularity: 1 SM = 4 partitions = 128 CUDA + 4 TC | Full GPU: 132 SMs (H100) share L2 | SM has private L1/Shared Mem (192 KB)

## Slide 4
TPU Core: Input Buffer + 128x128 Systolic Array
Weight-stationary dataflow: weights loaded once, inputs stream through, outputs drain
Weight Buffer (SRAM)
Load once per tile
Input Buffer (L1 SRAM)
128 x 128 Systolic Array
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
16,384 MACs/cycle
Accumulators + Output Buffer
TPU Core Energy Equation (per MAC):
E_tpu = E_weight_load/reuse + E_input_feed + E_systolic_mac + E_output_drain/array_size
E_tpu = 0.500/64 + 0.300 + 1.440 + 0.300/128
= 0.008 + 0.300 + 1.440 + 0.002 = 1.750 pJ/op (input-feed dominated overhead)
Model output (from build_tpu_cycle_energy at 7nm, L1-resident):
Config (one-time)
0.003 pJ/op
Weight load (amortized 64x)
0.016 pJ/op
Input feed (one edge, per cycle)
0.610 pJ/op
Systolic MAC (128x128)
1.440 pJ/op
Partial sum accumulation
0.006 pJ/op
Output drain (one edge)
0.010 pJ/op
TOTAL (core only)
2.085 pJ/op
Key Characteristics:
* No instruction fetch per operation (fixed-function)
* No register file arbitration (data flows spatially)
* Weight-stationary ONLY -- cannot do input/output stationary
* Input feed (0.610 pJ/op) dominates overhead -- each input must enter at array edge
* Granularity is LARGE: 128x128 = 16,384 MACs per cycle. Small workloads waste MACs.
Granularity: 1 MXU = 128x128 systolic array | Full TPU: 2 MXUs + Unified Buffer (24 MB) | Weight-stationary only

## Slide 5
KPU Tile: Input Buffer + 16x16 PE Array + SURE Network
Programmable domain flow: A/B/C-stationary, any SURE schedule, compile-time routed
EDDO L1 Stream Buffer (software-managed SRAM)
Streamer (vector -> token stream)
16 x 16 PE Array
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
256 MACs/cycle per tile
SURE network: PE-to-PE wires
KPU Tile Energy Equation (per MAC):
E_kpu = E_config/N_ops + 2 * E_pe_wire + E_domain_mac + E_local_reg
E_kpu = ~0 + 2 * 0.022 + E_mac(precision) + 0.009
BF16: 0.053 + 1.080 = 1.133 pJ/op | INT8: 0.053 + 0.675 = 0.728 pJ/op
Model output (from build_kpu_cycle_energy at 7nm, L1-resident, mixed precision):
Domain program load (1-time)
0.000 pJ/op (amortized)
Domain tracker (64 tiles)
0.001 pJ/op (amortized)
PE-to-PE transfer (x2 operands)
0.044 pJ/op
Local register write
0.009 pJ/op
INT8 MACs (70%)
0.473 pJ/op (weighted)
BF16 MACs (20%)
0.216 pJ/op (weighted)
FP32 MACs (10%)
0.216 pJ/op (weighted)
TOTAL (core only, mixed)
0.958 pJ/op
Key Characteristics:
* No instruction fetch per operation (domain program loaded once)
* No register file -- PE-to-PE wire transfer at 0.022 pJ (vs GPU's ~3 pJ/warp infrastructure)
* Programmable: A/B/C-stationary, any SURE schedule (vs TPU weight-stationary only)
* Small tile (256 MACs) = better utilization at batch=1 than TPU's 16,384 MACs
* Overhead is 5.5% of total -- 94.4% of energy is useful compute
Granularity: 1 tile = 16x16 = 256 MACs | Full KPU: 64 tiles (KPU-T64) to 768 tiles (KPU-T768) | Each tile has private L1 stream buffer

## Slide 6
Core Compute Energy: Side-by-Side at 7nm (No External Memory)
 | CPU Scalar | CPU AVX-512 | GPU CUDA | GPU TensorCore | TPU 128x128 | KPU 16x16
MAC energy (pJ) | 1.800 | 1.800 | 1.530 | 1.530 | 1.440 | 0.905*
Overhead (pJ/op) | 8.136 | 0.509 | 0.418 | 0.284 | 0.639 | 0.053
Total (pJ/op) | 9.936 | 2.309 | 1.948 | 1.814 | 2.085 | 0.958
Compute Efficiency | 18.1% | 78.0% | 78.5% | 84.4% | 69.4% | 94.4%
Amortization | 1 | 16 | 32 | 64 | 128-16K | 256
MACs per cycle | 1 | 16 | 128 | 256 | 16,384 | 256
Has instruction fetch | Yes | Yes | Yes | Yes | No | No
Has register file | Yes | Yes | 256KB | 256KB | No (PE) | No (PE)
Programmable schedule | N/A | N/A | N/A | N/A | Weight only | A/B/C
* KPU mixed precision: 70% INT8 (0.675) + 20% BF16 (1.080) + 10% FP32 (2.160) = 0.905 pJ avg
Energy per Op (pJ) -- Green = Compute, Gray = Overhead:
CPU Scalar
1.80
8.14
9.94 pJ
CPU AVX-512
1.80
0.51
2.31 pJ
GPU CUDA
1.53
0.42
1.95 pJ
GPU TC
1.53
1.81 pJ
TPU 128x128
1.44
0.64
2.08 pJ
KPU 16x16
0.91
0.96 pJ
Core Compute Takeaway (all at 7nm, no memory):
The MAC energy itself is comparable: 0.9-1.8 pJ across all architectures (2x range).
The overhead varies 150x (0.053 to 8.136 pJ). CPU scalar is worst; KPU is best.
KPU achieves 94% compute efficiency vs GPU TensorCore's 84% -- a 1.9x total energy advantage at same node.
The 20x argument requires adding memory hierarchy (domain 2) and system I/O (domain 3) advantages.