## Slide 1
The Energy Problem in Computing
Understanding Where Energy Goes in a CPU Pipeline
Key Insight:
The ALU -- where useful computation happens -- consumes only
~20% of total operation energy. The other 80% is overhead.
Instruction Frontend
Fetch + Decode ~40% of energy ~66% of transistors
Data Movement
Register File + Caches ~30% of energy
Useful Compute
ALU / FPU ~20% of energy
Source: Horowitz, ISSCC 2014 -- scaled to modern process nodes (4-7nm)

## Slide 2
The 5-Stage CPU Pipeline: A Stored-Program Machine
Random Access Memory Stored Program Machine (Von Neumann Architecture)
IF Instruction Fetch
ID Instruction Decode
EX Execute
MEM Memory Access
WB Write Back
L1 I-Cache (32-64 KB)
Register File (RF) 128-256 entries x 64-bit
ALU / FPU / SIMD
L1 D-Cache (32-64 KB)
L2 Cache (256 KB - 1 MB)
L3 / LLC (8 - 32 MB)
DRAM (DDR5 / LPDDR5)
FRONTEND
BACKEND
Key Architectural Observations
* Every operation requires an instruction fetch + decode cycle (the "instruction tax")
* The register file is accessed on BOTH sides: read before EX, write after EX
* WAR/RAW hazards in writeback add scoreboarding and forwarding energy
* ~66% of all transistors serve the frontend (fetch, decode, branch prediction, rename)

## Slide 3
Execute Stage Energy: The Useful Work
Register File READ (2 operands)
ALU / FPU FMA Operation
Register File WRITE (result)
Energy Equation for the Execute Stage:
E_execute = 2 x E_rf_read + E_alu + E_rf_write
Typical Energy Values by Process Technology (pJ per 32-bit FP32 FMA)
Process Node | RF Read (x2) | ALU (FMA) | RF Write | E_execute Total | ALU % of Total
28nm (IoT) | 2 x 1.8 = 3.6 | 4.0 | 2.0 | 9.6 pJ | 42%
16nm (Auto) | 2 x 1.2 = 2.4 | 2.7 | 1.3 | 6.4 pJ | 42%
7nm (Datacenter) | 2 x 0.8 = 1.6 | 1.8 | 0.9 | 4.3 pJ | 42%
5nm (Mobile SoC) | 2 x 0.6 = 1.2 | 1.5 | 0.7 | 3.4 pJ | 44%
4nm (GPU/AI) | 2 x 0.5 = 1.0 | 1.3 | 0.6 | 2.9 pJ | 45%
Takeaway:
Even in the execute stage alone, the ALU is less than half the energy.
Register file access (read 2 operands + write 1 result) costs more than the computation itself.
Values derived from Horowitz ISSCC 2014, scaled by TSMC process node capacitance ratios

## Slide 4
Frontend Energy: The Hidden Dominant Cost
L1 I-Cache Read
Instruction Decode
Branch Predict
Register Rename
--- FRONTEND (instruction overhead, paid for EVERY operation) ---
Frontend Energy Equation:
E_frontend = E_icache_read + E_decode + E_branch_predict + E_rename
Frontend vs Execute Energy Comparison (per scalar FP32 operation, 7nm)
Component | Energy (pJ) | Category | % of Total
L1 I-Cache Read (32B line) | 5.0 | Frontend | 
Instruction Decode | 2.0 | Frontend | 
Branch Prediction | 1.5 | Frontend | 
Register Rename / Scoreboard | 1.0 | Frontend | 
Frontend Subtotal | 9.5 | FRONTEND | 63%
Execute Stage (from Slide 3) | 4.3 | BACKEND | 29%
Pipeline/Clock/Wire | 1.2 | Overhead | 8%
Transistor Budget Allocation (typical OoO CPU):
Frontend: 66%
Backend: 20%
Caches: 14%
The CPU spends 2/3 of its energy and transistors on figuring out WHAT to compute, not computing it.

## Slide 5
Total CPU Energy per Operation: The Full Picture
Complete Energy Equation:
E_total = E_frontend + E_execute + E_memory + E_static
= (I-cache + Decode + Branch + Rename) + (2*RF_read + ALU + RF_write) + (Cache hierarchy) + (Leakage)
Energy Breakdown per Scalar FP32 Operation at 7nm (pJ):
I-cache: 5.0
Decode: 2.0
Branch: 1.5
Rename: 1.0
RF Read: 1.6
ALU: 1.8
RF Write: 0.9
Wire: 1.2
Frontend: 9.5 pJ (63%)
Execute: 4.3 pJ (29%)
The Architectural Question: What If We Eliminate the Frontend?
CPU (Stored Program)
~15 pJ / scalar FP32 op
Frontend: 9.5 pJ (63%)
Execute: 4.3 pJ (29%)
Overhead: 1.2 pJ (8%)
Every op pays full instruction tax
GPU (SIMT Parallel)
~1.65 pJ / FMA (TensorCore)
SIMT amortizes fetch over 32 threads
But adds coherence + scheduling
Operand collector still ~1.5x ALU
Still a stored-program machine
KPU (Domain Flow)
Target: <0.1 pJ / MAC
NO instruction fetch/decode
Data-driven token execution
Operands arrive at PE, not fetched
Eliminates the 63% frontend tax
Eliminating the instruction frontend is the key to achieving 10-20x energy efficiency