## Slide 1
Memory Technology Energy Comparison
LPDDR5 vs GDDR6 vs HBM3: Energy per Byte at the System Level
Why Memory Technology Dominates the Energy Comparison:
In the validation deck, KPU memory was 57% of total energy (LPDDR5 at 8 pJ/byte)
while GPU memory was 26% (HBM3 at 5.5 pJ/byte). This 45% difference in off-chip
energy per byte obscures the architectural comparison. To make a fair argument,
we must understand exactly what drives these numbers.
LPDDR5 / 5X
Package-on-Package (PoP)
Low-voltage I/O (0.5V)
4 channels x 16-bit
6.4-8.5 GT/s per pin
8.0-7.0 pJ/byte
Target: Edge / Automotive
GDDR6 / 6X / 7
Discrete chips on PCB
High-speed PCB traces (1.35V)
8 chips x 32-bit bus
16-32 Gbps per pin
14.0-18.0 pJ/byte
Target: Gaming / Consumer GPU
HBM2 / 3 / 3E
3D TSV stacking on interposer
Ultra-short wires (~100um)
1024-bit bus per stack
3.2-9.6 Gbps per pin
5.0-7.0 pJ/byte
Target: AI / HPC Datacenter
The energy per byte varies 3.6x across these technologies (5.0 to 18.0 pJ/byte). This is comparable to the entire architectural energy advantage we are trying to measure.

## Slide 2
DRAM Energy Anatomy: The Four Components Every Access Pays
Based on Vogelsang (MICRO 2010) and Horowitz (ISSCC 2014) -- all DRAM technologies share this structure
1. Row Activation
Open a row in the DRAM array: - Precharge bitlines to VDD/2 - Assert wordline (select row) - Sense amplifiers detect charge - Latch entire row (~8-16 KB)
~3-5 pJ/byte (amortized over burst)
2. Column Access
Select bytes within the open row: - Column decoder selects columns - Mux routes data to I/O gating - Burst length: 16 (LPDDR5) or 32 (HBM3) beats
~1-2 pJ/byte
3. I/O & Signaling
Drive data off the DRAM die: - I/O driver charges bus capacitance - Signal travels to SoC receiver - Energy = C_bus * V_swing^2 per bit - Dominant factor: wire length + voltage
~1-10 pJ/byte (varies with packaging)
4. PHY & Controller
SoC-side memory interface: - Clock/data recovery (CDR) - Serializer/deserializer (SerDes) - Training, calibration circuits - Command/address encoding
~1-3 pJ/byte
Total Energy per Byte:
E_total = E_row_activation/burst_length + E_column_access + E_io_signaling + E_phy_controller
What Varies Across Technologies:
Row Activation (~same)
All use same DRAM cell physics (capacitor + transistor). ~3-5 pJ/byte regardless of tech.
Column Access (~same)
Same array organization. Burst length affects amortization (BL16 for LPDDR5, BL32 for HBM3).
I/O Signaling (VARIES 10x!)
THIS is where the difference lives: LPDDR5: PoP, short wire, 0.5V swing GDDR6: PCB trace, long wire, 1.35V HBM3: TSV, ~100um, 1.1V but wide bus
PHY/Controller (varies 2-3x)
Complexity tracks signaling: LPDDR5: Simpler PHY, lower rate GDDR7: PAM3 SerDes, complex HBM3: Many channels, simpler/pin
Key Insight: The DRAM core energy (row + column) is ~4-7 pJ/byte for ALL technologies. The 3.6x range (5 to 18 pJ/byte) comes almost entirely from I/O signaling and packaging.

## Slide 3
LPDDR5/5X: Low-Power Package-on-Package Memory
SoC / Processor Die
LPDDR5 PHY Ch0
LPDDR5 PHY Ch1
LPDDR5 PHY Ch2
LPDDR5 PHY Ch3
Memory Controller (4-channel, 64-bit total)
CPU / GPU / NPU Cores (compute logic)
LPDDR5 DRAM (Package-on-Package)
DRAM Die 0 (16-bit)
DRAM Die 1 (16-bit)
DRAM Die 2 (16-bit)
DRAM Die 3 (16-bit)
Wire: ~1-3 mm (PoP solder balls) | V_IO: 0.5V (LPDDR5) / 0.35V (LPDDR5X)
Energy Breakdown per Byte (LPDDR5 @ 6400 MT/s)
Component | Energy (pJ/B) | % of Total | Key Driver
Row Activation | 3.2 | 40% | DRAM cell physics (same as all)
Column Access | 1.2 | 15% | Burst length 16, column mux
I/O Signaling | 1.8 | 22% | 0.5V swing, short PoP wire (~2mm)
PHY / Controller | 1.0 | 13% | Simple PHY, 4 channels
Clock / Refresh | 0.8 | 10% | CK differential, tREFI refresh
TOTAL | 8.0 | 100% | 
Row: 3.2
Col: 1.2
I/O: 1.8
PHY: 1.0
Clk: 0.8
Key LPDDR5 Characteristics:
Low I/O voltage: 0.5V (LPDDR5) / 0.35V (LPDDR5X)
E_io = C_wire * V^2 -> 0.5V is 7.3x less than GDDR6's 1.35V
Short wires: Package-on-Package stacking = ~1-3 mm trace
vs GDDR6 PCB: ~20-50 mm | vs HBM TSV: ~0.05-0.1 mm
Narrow bus: 4 channels x 16-bit = 64-bit total bus width
Lower bandwidth (25-34 GB/s) but very power-efficient per byte
LPDDR5X improvement: Lower V_IO (0.35V) -> ~7.0 pJ/byte (12% better)

## Slide 4
GDDR6/6X/7: High-Speed Discrete Graphics Memory
GPU Die
Memory Controller (256-384 bit bus)
GDDR PHY (SerDes, PAM4/PAM3)
SMs / Compute Units (CUDA cores, TensorCores)
PCB Traces 20-50 mm
GDDR6 Chip 0 (32b)
GDDR6 Chip 1 (32b)
GDDR6 Chip 2 (32b)
GDDR6 Chip 3 (32b)
GDDR6 Chip 4 (32b)
GDDR6 Chip 5 (32b)
GDDR6 Chip 6 (32b)
GDDR6 Chip 7 (32b)
8 chips x 32-bit = 256-bit bus
Wire: 20-50 mm PCB | V_IO: 1.35V (GDDR6), PAM4 (GDDR6X), PAM3 (GDDR7)
Energy per Byte (pJ/B)
Component | GDDR6 | GDDR6X | GDDR7
Row Activation | 3.5 | 3.5 | 3.2
Column Access | 1.5 | 1.5 | 1.3
I/O Signaling | 6.5 | 9.0 | 5.8
PHY / Controller | 2.0 | 2.5 | 2.2
Clock / Refresh | 1.5 | 1.5 | 1.5
TOTAL | 15.0 | 18.0 | 14.0
Row: 3.5
Col: 1.5
I/O: 9.0
PHY: 2.5
Clk: 1.5
GDDR6X: I/O is 50% of total energy
Why GDDR I/O Energy Is So High:
1. Long PCB traces (20-50 mm):
Capacitance ~ 1-2 pF per trace (vs ~0.05 pF for HBM TSV)
E = C * V^2 per transition = 2 pF * 1.35^2 = 3.6 pJ/bit
2. High I/O voltage (1.35V for GDDR6):
Compared to 0.5V for LPDDR5: (1.35/0.5)^2 = 7.3x more energy per bit
This is pure physics: E = C*V^2, voltage dominates
3. PAM4 (GDDR6X) adds complexity:
4-level signaling requires tighter voltage margins + more complex receivers
Higher BW per pin, but MORE energy per bit (18 vs 15 pJ/byte)
4. PAM3 (GDDR7) partially recovers:
3-level signaling: 50% better noise margin than PAM4
Combined with lower voltage -> 14 pJ/byte (best GDDR)

## Slide 5
HBM2/3/3E: 3D-Stacked Memory on Silicon Interposer
Package Substrate / BGA
Silicon Interposer (65nm passive Si, ~30mm x 30mm)
GPU / Accelerator Die
HBM PHY (per-stack controller)
Compute Logic (SMs, TensorCores)
Die 0
Die 1
Die 2
Die 3
TSV 1024-bit
Base
Die 0
Die 1
Die 2
Die 3
TSV 1024-bit
Base
Die 0
Die 1
Die 2
Die 3
TSV 1024-bit
Base
HBM3 Stacks (3-6 stacks, 8-12 dies each)
TSV pitch: ~5-10 um | Wire length: ~50-100 um (vertical) + ~5-15 mm (interposer) | V_IO: 1.1V
Energy per Byte (pJ/B)
Component | HBM2 | HBM2E | HBM3 | HBM3E
Row Activation | 2.8 | 2.6 | 2.2 | 2.0
Column Access | 1.0 | 1.0 | 0.8 | 0.8
I/O (TSV+Interp) | 1.5 | 1.3 | 1.0 | 0.8
PHY / Controller | 1.0 | 1.0 | 0.9 | 0.8
Clock / Refresh | 0.7 | 0.6 | 0.6 | 0.6
TOTAL | 7.0 | 6.5 | 5.5 | 5.0
Row: 2.2
Col: 0.8
I/O: 1.0
PHY: 0.9
Clk: 0.6
HBM3: Row activation is 40% -- I/O is only 18%
Why HBM Achieves the Lowest Energy per Byte:
1. Ultra-short I/O path (TSV):
TSV length: ~50 um (vs 20-50 mm for GDDR PCB)
Wire capacitance: ~50 fF (vs 2 pF for PCB)
-> 40x less capacitance = 40x less I/O energy
2. Ultra-wide bus (1024-bit per stack):
Low speed per pin (3.2-9.6 Gbps)
-> Simple NRZ signaling (no PAM4 overhead)
-> Simpler PHY per pin, lower per-bit energy
3. DRAM process optimization:
HBM uses latest DRAM process node
Smaller cells -> less charge -> less row energy
The Trade-Off: Cost vs Energy:
HBM3: 5.5 pJ/B | 3.35 TB/s | 12x cost
LPDDR5: 8.0 pJ/B | 25 GB/s | 2x cost
GDDR6: 15.0 pJ/B | 128 GB/s | 2x cost
HBM is 2.7x more energy-efficient than GDDR6
but costs 6x more per GB.
LPDDR5 is 1.9x more energy-efficient than GDDR6
at the same cost tier -- but 100x less bandwidth.
For energy-optimized AI (KPU), LPDDR5 at 8 pJ/B
is within 1.45x of HBM3 at 5.5 pJ/B, at 6x lower cost.
Sources: Vogelsang MICRO 2010, Horowitz ISSCC 2014, JEDEC LPDDR5/GDDR6/HBM3 specs, vendor datasheets (Micron, SK hynix, Samsung)