## Slide 1
The Register File IS the Architecture
Why 256 KB of Banked SRAM Defines GPU Energy -- and What TPU/KPU Do Instead
The Central Question:
Every compute architecture must deliver operands to ALUs. The question is HOW:
GPU: Centralized 256 KB banked SRAM shared by 2048 threads, accessed via
address decode -> bank arbitration -> operand collector -> crossbar -> ALU
TPU/KPU: Distributed PE-local registers (latches). Each PE has 2-4 registers.
Data arrives via spatial wiring (compile-time routed). No shared SRAM.
CPU
Small RF (16-64 regs) Multi-ported SRAM Per-core, private Overhead: moderate (addressed by SIMD width)
GPU SM
MASSIVE RF (64K regs = 256 KB) 32-banked SRAM Shared by 2048 threads Overhead: LARGE (hidden by amortization)
TPU / KPU
DISTRIBUTED (PE-local latches) No shared SRAM structure No address decode or arbitration Overhead: NEAR ZERO (operands arrive spatially)
All comparisons at 7nm TSMC N7. Core compute only (no external memory).

## Slide 2
CPU: Small Register File, Amortized by SIMD Width
CPU Core (1 of N)
Register File: 16 architectural (x86-64) + ~100 physical (rename) Multi-ported SRAM: 2 read + 1 write per cycle Size: ~1-2 KB | Private to this core
Scalar ALU FP32 FMA 1 op/cycle
SIMD ALU (AVX-512) 16 x FP32 FMA 16 ops/cycle
Instruction Pipeline: I-cache -> Decode -> Dispatch -> Rename -> Issue
L1 I-Cache (32 KB)
L1 D-Cache (48 KB)
L2 Cache (256 KB - 1 MB, exclusive to core)
Energy Equations at 7nm:
Scalar (1 op/instr):
E = E_ifetch + E_decode + 2*E_rf_read + E_alu + E_rf_write
= 0.540 + 0.288 + 2*1.013 + 1.800 + 1.215
= 5.868 pJ (overhead) + 1.800 pJ (ALU) = 7.668 pJ/op
x2 instructions per FMA = 9.936 pJ/op | Eff: 18%
AVX-512 (16 ops/instr):
E = (E_ifetch + E_decode + 2*E_vrf_read + E_vrf_write)/16 + E_alu
= (0.540 + 0.288 + 2*1.013 + 1.215) / 16 + 1.800
= 0.254 pJ (overhead) + 1.800 pJ (ALU) = 2.054 pJ/op
x2 instructions per FMA / 16 = 2.309 pJ/op | Eff: 78%
CPU RF is SMALL (~1-2 KB) and PRIVATE:
* Multi-ported but only 2R+1W per cycle
* No bank conflicts (only 1 thread using it)
* No operand collector (data immediately available)
* SIMD amortizes the overhead over 16 lanes
The CPU RF is a solved problem at ~1-2 KB.
The GPU scales this to 256 KB -- that changes everything.
Granularity: 1 core | RF: 1-2 KB private | 1 scalar + 1 SIMD ALU | Private L1i + L1d + L2

## Slide 3
GPU SM: 256 KB Banked SRAM Register File + Delivery Infrastructure
The register file IS the SM. Everything else exists to feed it or be fed by it.
Register File: 64K x 32-bit = 256 KB Banked SRAM
Bank 0 2K regs
Bank 1 2K regs
Bank 2 2K regs
Bank 3 2K regs
Bank 4 2K regs
Bank 5 2K regs
Bank 6 2K regs
Bank 7 2K regs
Bank 8 2K regs
Bank 9 2K regs
Bank 10 2K regs
Bank 11 2K regs
Bank 12 2K regs
Bank 13 2K regs
Bank 14 2K regs
Bank 15 2K regs
Bank 16 2K regs
Bank 17 2K regs
Bank 18 2K regs
Bank 19 2K regs
Bank 20 2K regs
Bank 21 2K regs
Bank 22 2K regs
Bank 23 2K regs
Bank 24 2K regs
Bank 25 2K regs
Bank 26 2K regs
Bank 27 2K regs
Bank 28 2K regs
Bank 29 2K regs
Bank 30 2K regs
Bank 31 2K regs
32 banks | 2048 regs/bank | 8 KB SRAM per bank | All banks active every cycle
Operand Collector (x4)
32-wide Crossbar + Bank Arb
128 CUDA Cores + 4 TensorCores (shared across 4 partitions)
Why 256 KB? The Latency-Hiding Requirement:
Thread concurrency hides memory latency:
HBM access: ~400 cycles at 1.5 GHz
To hide this: need ~32 warps ready to execute
Each warp: 32 threads x 32 registers x 4 bytes = 4 KB
Total: 32 warps x 4 KB = 128 KB minimum
Actual: 64 warps x 4 KB = 256 KB (headroom)
This is NOT a design choice -- it is a REQUIREMENT.
Fewer registers = fewer resident threads = exposed latency = stalls.
The GPU MUST have 256 KB of fast, banked SRAM to function.
Infrastructure Required to Serve 256 KB RF:
32 SRAM banks
Parallel access for 32 threads per warp
Bank arbitration logic
Resolve conflicts when 2+ warps access same bank
4 Operand collectors
Buffer partially-read operands until all 32 are ready
32-wide crossbar
Route operands from any bank to any ALU lane
4 Warp schedulers
Select which of 16 warps to issue each cycle
4 Scoreboards
Track RAW/WAW/WAR hazards across all active warps
The GPU cannot shrink or remove the register file. It is the latency-hiding mechanism.
Every component above (banks, arbitration, collectors, crossbar, schedulers, scoreboards) exists
solely to serve this 256 KB SRAM. This is the architecture the TPU and KPU eliminate.

## Slide 4
TPU / KPU: Distributed PE-Local Registers Replace Shared SRAM
The spatial schedule eliminates resource conflicts -- each PE owns its data
TPU: 128x128 Systolic Array (Weight-Stationary)
PE
W reg
MAC
Accum
PE
W reg
MAC
Accum
PE
W reg
MAC
Accum
PE
W reg
MAC
Accum
PE
W reg
MAC
Accum
PE
W reg
MAC
Accum
Inputs stream left-to-right | Partial sums flow top-to-bottom
Total storage: 16,384 PEs x 2 regs x 32b = 128 KB
But: each register is a LOCAL latch inside its PE
* No address decode (hardwired)
* No bank arbitration (no sharing)
* No operand collector (data already local)
* No crossbar (PE-to-PE wire, compile-time routed)
* Weight-stationary: W loaded once, reused 128+ times
KPU: 16x16 PE Array (Programmable Domain Flow)
PE
A
B
MAC
C
PE
A
B
MAC
C
PE
A
B
MAC
C
PE
A
B
MAC
C
PE
A
B
MAC
C
PE
A
B
MAC
C
SURE network: compile-time routed wires between PEs (~0.02 pJ/transfer)
Total storage: 256 PEs x 4 regs x 32b = 4 KB per tile
64 tiles = 16,384 PEs x 4 regs = 256 KB total (same as GPU!)
But: each register is a LOCAL latch inside its PE
* Same benefits as TPU (no decode, no arbitration, ...)
* PLUS: programmable schedule (A/B/C-stationary)
* PLUS: any SURE recurrence equation, not just GEMM
* Smaller tile (256 MACs) = better utilization at batch=1
The Fundamental Difference: Shared SRAM vs Distributed Latches
 | GPU SM | TPU Array | KPU Tile
Total register storage | 256 KB | 128 KB | 256 KB (64 tiles)
Storage structure | Centralized banked SRAM | PE-local latches | PE-local latches
Access mechanism | Address decode + bank arb + collector + crossbar | Spatial wiring (weight-stationary) | SURE network (compile-time routed)
Concurrent accessors | 2048 threads (contention!) | 16,384 PEs (no contention) | 16,384 PEs (no contention)
Infrastructure needed | Scheduler, scoreboard, collector, crossbar | Input/output buffers only | Streamer + L1 buffer only
Can GPU copy this? | --- | NO (would require removing SIMT model) | NO (would require removing SIMT model)

## Slide 5
Dynamic Energy: The Per-Operation Cost of Operand Delivery
Same computation, different operand delivery -- all at 7nm, per FP32 MAC
GPU: Operand Delivery Chain (per warp instruction, CUDA path)
Warp Scheduler
0.875 pJ
Score- board
0.525 pJ
Addr Gen x3
1.050 pJ
Bank Arbitr.
0.525 pJ
SRAM Read x2
0.562 pJ
Operand Collector
1.400 pJ
Cross- bar
0.700 pJ
ALU (32 MACs)
1.530 /op pJ
Result Route+WB
0.863 pJ
Overhead per warp: 6.500 pJ | Per MAC (/32): 0.203 pJ | ALU: 1.530 pJ | Total: 1.733 pJ/op | Eff: 88%
TPU: Operand Delivery (spatial, weight-stationary)
Input Buffer
0.300 pJ
PE wire (spatial)
~0.05 pJ
Systolic MAC
1.440 /op pJ
PE wire (drain)
~0.01 pJ
Overhead: ~0.36 pJ/op | Total: ~1.80 pJ/op | Eff: 80% No scheduler, no scoreboard, no collector, no crossbar.
KPU: Operand Delivery (SURE network, compile-time routed)
L1 Stream Buffer
~0.01 pJ
PE wire (SURE)
0.022 pJ
Domain Flow MAC
0.675- 2.160 pJ
Local reg write
0.009 pJ
Overhead: ~0.053 pJ/op | Total: 0.958 pJ/op (mixed) | Eff: 94% Same zero-infrastructure as TPU, plus programmable schedule.
Operand delivery overhead per MAC at 7nm:
GPU: 0.203 pJ (9 pipeline stages, all serving 256 KB SRAM) | TPU: ~0.36 pJ (buffer + wire) | KPU: ~0.053 pJ (wire + local reg)
GPU-to-KPU overhead ratio: 4x. This is the structural advantage the GPU cannot replicate without removing SIMT.

## Slide 6
Static Power: The Always-On Cost of 256 KB SRAM
A separate argument from dynamic energy: leakage power is paid regardless of utilization
What is Static Power?
Every transistor in the 256 KB SRAM leaks current
even when no computation is happening.
This is a consequence of FinFET physics at 7nm:
P_static = N_transistors * I_leak * V_dd
At 7nm FinFET, typical SRAM leakage:
~0.2 W per MB of SRAM (typical 7nm datacenter)
256 KB SRAM -> ~50 mW per SM
This leakage is paid:
* When computing (overlaps with dynamic energy)
* When waiting for memory (100s of cycles)
* When partially utilized (batch=1 workloads)
* When idle (unless power-gated -- but GPU SMs
rarely power-gate RF due to thread context)
Scaling to Full GPU (H100-class, 7nm):
Per SM:
RF SRAM: 256 KB
Leakage: ~50 mW
At 1.5 GHz: 33.3 pJ/cycle
At 128 MACs/cycle: 0.26 pJ/MAC (CUDA)
At 256 MACs/cycle: 0.13 pJ/MAC (TC)
Full GPU (132 SMs):
Total RF: 132 x 256 KB = 33 MB SRAM
Total RF leakage: 132 x 50 mW = 6.6 W
Share of 700W TDP: 0.9%
+ Shared L1/SMEM (192 KB x 132 = 25 MB): ~5 W
+ L2 Cache (50 MB): ~10 W
Total SRAM leakage: ~22 W (3% of TDP)
TPU/KPU Comparison: Distributed Latches Have ~10x Lower Leakage
PE-local latches (flip-flops) leak ~10x less than SRAM cells per bit, because:
* SRAM cell: 6 transistors, continuous feedback loop, both P/N paths leak
* Flip-flop latch: simpler structure, clock-gated when PE is idle
Furthermore, spatial architectures enable fine-grained power gating:
* GPU: cannot power-gate individual SM register banks (thread context would be lost)
* TPU: can power-gate unused rows/columns of systolic array (but array is large)
* KPU: can power-gate individual tiles (16x16 = fine granularity, 256 MACs per tile)
Important: Static power is a secondary effect (~0.13-0.26 pJ/MAC) compared to
dynamic RF infrastructure cost (~0.20 pJ/MAC overhead). The dynamic cost is the primary argument.
Static power matters most at low utilization (batch=1, idle SMs, memory-bound workloads).

## Slide 7
Core Compute Energy Summary: All at 7nm, No External Memory
 | CPU Scalar | CPU AVX-512 | GPU CUDA | GPU TC | TPU 128x128 | KPU 16x16
RF / operand storage | ~1 KB private SRAM | ~1 KB private SRAM | 256 KB banked SRAM | 256 KB banked SRAM | 128 KB PE latches | 4 KB/tile PE latches
Operand delivery | 2R+1W ports | 2R+1W vector | 32-bank +collector +crossbar | 32-bank +collector +crossbar | Spatial wire | SURE wire
MAC energy (pJ) | 1.800 | 1.800 | 1.530 | 1.530 | 1.440 | 0.905*
Overhead (pJ/op) | 8.136 | 0.509 | 0.418 | 0.284 | 0.639 | 0.053
of which: RF infra | 4.050 | 0.253 | 0.127 | 0.075 | ~0.01 | ~0.009
Static RF (pJ/MAC) | ~0 | ~0 | 0.260 | 0.130 | ~0.03 | ~0.01
TOTAL (pJ/op) | 9.936 | 2.309 | 1.948 | 1.814 | 2.085 | 0.958
Compute Efficiency | 18% | 78% | 79% | 84% | 69% | 94%
Energy per Op: Green = MAC | Orange = RF Infrastructure | Gray = Other Overhead | Red = Static
CPU Scalar
1.80
4.05
4.09
9.94
CPU AVX-512
1.80
2.31
GPU CUDA
1.53
0.26
2.21
GPU TC
1.53
1.94
TPU
1.44
0.63
2.11
KPU
0.91
0.97
Core Compute Takeaway:
The 256 KB banked SRAM register file and its delivery infrastructure (operand collector, crossbar, bank arbitration) is the GPU's structural energy cost. It adds ~0.13-0.26 pJ/MAC in dynamic overhead plus ~0.13-0.26 pJ/MAC in static leakage.
TPU/KPU eliminate this entirely with distributed PE-local latches. This is a 1.9x core compute advantage (GPU TC: 1.81 vs KPU: 0.96 pJ/op) that the GPU cannot close without abandoning SIMT.
* KPU mixed precision: 70% INT8 + 20% BF16 + 10% FP32. Single-precision BF16 KPU: ~1.13 pJ/op.