## Slide 1
Energy Model Validation: Checking Our Numbers
Every parameter, every equation, every assumption -- spelled out for verification
Methodology
1. Base ALU Energy: Horowitz ISSCC 2014, scaled by process node capacitance (C*V^2)
E_base(node) = {3nm: 1.20, 4nm: 1.30, 5nm: 1.50, 7nm: 1.80, 16nm: 2.70} pJ
2. Circuit Type Multiplier: Accounts for design complexity vs efficiency trade-off
E_alu = E_base * multiplier (x86: 2.50x, cuda: 0.95x, tensor: 0.85x, systolic: 0.80x, domain: 0.75x)
3. Architecture-Specific Overhead: Per-cycle infrastructure energy
CPU: instruction pipeline + register file (per instruction, amortized over SIMD width)
GPU: warp scheduler + scoreboard + operand collector + crossbar (per warp, amortized over 32/64 MACs)
TPU: weight loading + input feeding + output draining (per tile, amortized over MxM MACs)
KPU: PE-to-PE wire + local register write + EDDO memory (per op, near-zero overhead)
4. Memory Hierarchy: Cache/scratchpad + off-chip access, workload-dependent
Reference Workload for All Evaluations
Operations: 1,000,000 MACs | Data transferred: 1,048,576 bytes (1 MB) | Operating mode: DRAM-resident
This workload is large enough to amortize fixed overheads (kernel launch, domain program load)
KPU precision mix: 70% INT8, 20% BF16, 10% FP32 (as configured in kpu.py)
Source: graphs/hardware/technology_profile.py, graphs/hardware/cycle_energy/{cpu,gpu,tpu,kpu}.py

## Slide 2
Parameter Sources: Process, Circuit, and Memory Technology
Architecture Configuration (from technology_profile.py)
Parameter | CPU (7nm) | GPU (4nm) | TPU (7nm) | KPU (7nm) | Formula
Process Node | 7nm (TSMC N7) | 4nm (TSMC N4P) | 7nm | 7nm | ---
E_base (FP32 ALU) | 1.80 pJ | 1.30 pJ | 1.80 pJ | 1.80 pJ | PROCESS_NODE_BASE_ENERGY_PJ[nm]
Circuit Multiplier | x86_perf: 2.50x | tensor_core: 0.85x | systolic: 0.80x | domain_flow: 0.75x | CIRCUIT_TYPE_MULTIPLIER[type]
E_mac (effective) | 1.80 pJ | 1.105 pJ | 1.440 pJ | 1.350 pJ | E_base * multiplier
Memory Technology | DDR5 | HBM3 | HBM2e | LPDDR5 | ---
Off-chip (pJ/byte) | 20.0 | 5.5 | 6.5 | 8.0 | MemoryType spec
SRAM/L1 (pJ/byte) | 0.400 | 0.2514 | 0.400 | 0.400 | get_sram_energy_per_byte_pj()
I-fetch (pJ) | 0.540 | 0.488 | 0.180 | 0.090 | E_base * pipeline_factor
RF read (pJ) | 1.012 | 0.812 | 0.900 | 0.720 | E_base * rf_factor
RF write (pJ) | 1.215 | 0.975 | 0.900 | 0.720 | E_base * rf_factor
Critical Observations About Parameter Consistency
1. Process Node Asymmetry: GPU at 4nm (E_base=1.30) vs TPU/KPU at 7nm (E_base=1.80)
The 4nm GPU has a 28% base energy advantage before any circuit multiplier is applied.
For fair comparison, all architectures should be evaluated at the same process node.
2. Memory Technology Asymmetry: GPU uses HBM3 (5.5 pJ/byte) vs KPU uses LPDDR5 (8.0 pJ/byte)
The GPU has a 31% memory energy advantage per byte. KPU compensates via EDDO (no tag lookup),
but the raw off-chip cost is higher. HBM variant of KPU would close this gap.
3. MAC Energy: TPU systolic = 1.440 pJ, KPU domain_flow = 1.350 pJ (both at 7nm)
These ARE comparable, as expected. The 0.75x vs 0.80x multiplier reflects domain flow's
slightly simpler PE design (no weight-stationary control logic).
4. GPU tensor_core_mac = 1.105 pJ. This is E_base(4nm)*0.85 = 1.30*0.85.
The Horowitz-derived switching energy for FP16 mult + FP32 add is 0.34 pJ.
The model uses the circuit-multiplier method, not Horowitz component analysis.

## Slide 3
Energy Equations: Every Term Spelled Out
CPU (7nm scalar)
E_cpu = 2*(E_ifetch + E_idecode) + 2*E_rf_read + E_alu + E_rf_write + E_memory
= 2*(0.540 + 0.288) + 2*1.012 + 1.800 + 1.215 + E_mem
= 1.656 (frontend) + 3.240 (RF) + 1.800 (ALU) + 1.280 (mem) = 11.22 pJ/op | Compute eff: 16.0%
GPU TensorCore (4nm)
E_gpu_tc = (E_ifetch + E_idecode + E_sched + E_scoreboard + E_addrgen + E_collector + E_arb + E_route)/64 + E_mac + (E_result_route + E_rf_write)/64 + E_simt + E_memory
= 0.0117 (front) + 0.0328 (fetch) + 1.1050 (ALU) + 0.0100 (WB) + 0.1135 (SIMT) + 0.4564 (mem)
= 1.7294 pJ/op | ALU = 1.105 pJ = 1.30 * 0.85 | Compute eff: 63.9%
GPU CUDA Core (4nm)
E_gpu_cuda = (E_ifetch + E_idecode + E_sched + E_scoreboard + E_addrgen + E_collector + E_arb + E_route)/32 + E_mac + (E_result_route + E_rf_write)/32 + E_simt + E_memory
= 0.0234 (front) + 0.0783 (fetch) + 1.1050 (ALU) + 0.0170 (WB) + 0.1293 (SIMT) + 0.4564 (mem) = 1.8094 pJ/op | Compute eff: 61.1%
TPU Systolic (7nm)
E_tpu = E_config/N_ops + E_weight_load/reuse + E_input_feed + E_systolic_mac + E_output_drain + E_memory
= 0.6390 (ctrl+data_move) + 1.4458 (ALU) + 0.7392 (mem) | MAC = 1.440 pJ = 1.80 * 0.80
= 2.8240 pJ/op | Compute eff: 51.2%
KPU Domain Flow (7nm)
E_kpu = E_config/N_ops + 2*E_pe_transfer + E_domain_mac + E_local_write + E_eddo_memory
= 0.0533 (spatial+config) + 0.9045 (ALU) + 1.2583 (mem) | MAC(BF16) = 1.350*0.8 = 1.080 pJ = 1.80 * 0.75 * 0.8
= 2.2161 pJ/op (mixed: 70% INT8 + 20% BF16 + 10% FP32) | Compute eff: 40.8%

## Slide 4
Numerical Evaluation: 1,000,000 ops, 1,048,576 bytes
Category (pJ/op) | CPU scalar (7nm) | CPU AVX-512 (7nm) | GPU CUDA (4nm) | GPU TC (4nm) | TPU (7nm) | KPU (7nm)
Frontend | 1.6560 | 0.1035 | 0.0234 | 0.0117 | --- | ---
Operand Fetch | 4.0500 | 0.2531 | 0.0783 | 0.0328 | --- | ---
Compute (ALU) | 1.8000 | 1.8000 | 1.1050 | 1.1050 | 1.4458 | 0.9045
Writeback | 2.4300 | 0.1519 | 0.0170 | 0.0100 | --- | ---
SIMT Overhead | --- | --- | 0.1293 | 0.1135 | --- | ---
Systolic Ctrl | --- | --- | --- | --- | 0.6390 | ---
Spatial/Config | --- | --- | --- | --- | --- | 0.0533
Memory | 1.2799 | 1.2799 | 0.4564 | 0.4564 | 0.7392 | 1.2583
TOTAL | 11.2159 | 3.5884 | 1.8094 | 1.7294 | 2.8240 | 2.2161
Compute Efficiency | 16.0% | 50.2% | 61.1% | 63.9% | 51.2% | 40.8%
Energy ratio vs GPU TC | 6.49x | 2.07x | 1.05x | 1.00x | 1.63x | 1.28x
Analysis: What Drives Each Architecture's Total
Dominant energy category per architecture:
CPU scalar: Operand Fetch = 36% | CPU AVX-512: Compute (ALU) = 50%
GPU CUDA: Compute (ALU) = 61% | GPU TC: Compute (ALU) = 64%
TPU: Compute (ALU) = 51% | KPU: Memory = 57%
Key: GPU SIMT overhead includes kernel launch (100K pJ, amortized over 1M ops = 0.10 pJ/op).
KPU memory is 57% of total because LPDDR5 costs 8.0 pJ/byte vs GPU's HBM3 at 5.5 pJ/byte.
The KPU's 70% INT8 mix lowers its average MAC to 0.90 pJ vs TPU's pure 1.44 pJ systolic MAC.

## Slide 5
Compute Efficiency and Known Model Gaps
Compute Efficiency = ALU Energy / Total Energy (what fraction is useful work)
CPU scalar
16.0%
overhead: 84.0%
CPU AVX-512
50.2%
overhead: 49.8%
GPU CUDA
61.1%
overhead: 38.9%
GPU TC
63.9%
overhead: 36.1%
TPU
51.2%
overhead: 48.8%
KPU (mixed)
40.8%
overhead: 59.2%
Known Model Gaps and Issues to Resolve
1. GPU SM Baseline Power Not Modeled
The 64K register file (256 KB SRAM), 4 operand collectors, 4 scoreboards, and 32-bank crossbar
draw continuous power even between instructions. This static infrastructure energy is NOT captured
in the per-instruction cycle model. It would increase GPU total and decrease GPU compute efficiency.
2. Process Node Mismatch
GPU at 4nm (E_base=1.30) vs TPU/KPU at 7nm (E_base=1.80). The GPU gets a 28% base advantage.
Need: same-node comparison (all at 4nm or all at 7nm) to isolate architectural effects.
3. Memory Technology Mismatch
GPU HBM3 (5.5 pJ/byte) vs KPU LPDDR5 (8.0 pJ/byte). The GPU has 31% lower off-chip energy.
At 1MB data, memory is 26% of GPU energy but 57% of KPU energy. Need: same memory comparison.
4. KPU Precision Mix
KPU default is 70% INT8 + 20% BF16 + 10% FP32 (avg MAC = 0.90 pJ).
TPU is pure systolic at 1.44 pJ. Single-precision comparison would change the efficiency ratio.