## Slide 1
GPU Energy: From Instruction Tax to Data Movement Tax
How Thread Concurrency Hides Latency but Shifts the Energy Problem
The GPU Bargain:
GPUs reduce instruction frontend overhead by amortizing one instruction
across 32 threads (a warp). But to hide memory latency, they run hundreds
of concurrent threads -- each needing its own registers.
The result: 64K registers per SM, fed through banked SRAM with operand
collectors. This data movement infrastructure is always active.
CPU: Frontend-Heavy
~15 pJ per scalar FP32 op
63% energy in instruction frontend
I-cache, decode, branch predict, rename
Small register file (16-64 entries)
GPU: Data-Movement-Heavy
~1.65 pJ per TensorCore MAC
Frontend amortized over 32 threads
But: 64K registers, banked SRAM,
operand collectors, crossbar routing
-->
Both architectures are stored-program machines -- operands must be explicitly fetched

## Slide 2
Streaming Multiprocessor (SM) Architecture: H100-Class
Each SM is divided into 4 independent partitions -- each a complete SIMD execution pipeline
Partition 0
Warp Scheduler
Scoreboard (RAW/WAW/WAR)
Operand Collector (gather + buffer)
Register Bank (16K regs)
Crossbar (32-wide routing)
32 CUDA Cores
1 Tensor Core (64 MACs)
Result Writeback
^ RF
Partition 1
Warp Scheduler
Scoreboard (RAW/WAW/WAR)
Operand Collector (gather + buffer)
Register Bank (16K regs)
Crossbar (32-wide routing)
32 CUDA Cores
1 Tensor Core (64 MACs)
Result Writeback
^ RF
Partition 2
Warp Scheduler
Scoreboard (RAW/WAW/WAR)
Operand Collector (gather + buffer)
Register Bank (16K regs)
Crossbar (32-wide routing)
32 CUDA Cores
1 Tensor Core (64 MACs)
Result Writeback
^ RF
Partition 3
Warp Scheduler
Scoreboard (RAW/WAW/WAR)
Operand Collector (gather + buffer)
Register Bank (16K regs)
Crossbar (32-wide routing)
32 CUDA Cores
1 Tensor Core (64 MACs)
Result Writeback
^ RF
Shared L1 Cache / Shared Memory -- 192 KB (configurable split)
L2 Cache -- 50 MB (shared across all 132 SMs)
HBM3 -- 80 GB (3.35 TB/s bandwidth)
Key SM Numbers (H100)
64K registers per SM (256 KB) | 2048 max resident threads | 64 max warps | 128 CUDA cores + 4 TensorCores | 32 register banks
Every cycle: 4 warp schedulers issue 4 instructions -> feeding 128 CUDA cores or 4 TensorCores simultaneously

## Slide 3
The 64K Register File: Banked SRAM Feeding the SIMD Engine
256 KB of register storage per SM, organized as 32 banks to support concurrent warp access
32 Register Banks (8 KB SRAM each)
Bank 0
Bank 1
Bank 2
Bank 3
Bank 4
Bank 5
Bank 6
Bank 7
Bank 8
Bank 9
Bank 10
Bank 11
Bank 12
Bank 13
Bank 14
Bank 15
Bank 16
Bank 17
Bank 18
Bank 19
Bank 20
Bank 21
Bank 22
Bank 23
Bank 24
Bank 25
Bank 26
Bank 27
Bank 28
Bank 29
Bank 30
Bank 31
Thread 0 -> Bank 0, Thread 1 -> Bank 1, ... Thread 31 -> Bank 31
Bank Conflict: When 2+ threads in a warp access the same bank, accesses are serialized -> variable latency -> needs buffering
Operand Delivery Pipeline (per warp instruction)
1. Scoreboard Lookup
Check RAW/WAW/WAR hazards for this warp
2. Register Address Gen
Decode src1, src2, dst register IDs (x32 threads)
3. Bank Arbitration
Detect & resolve bank conflicts across 32 threads
4. SRAM Read (32 banks)
Read 32 x 32-bit operands from banked register file
5. Operand Collector
Buffer operands until ALL 32 are ready (variable latency)
6. Crossbar Routing
Route 32 operands from collector to SIMD lanes
7. SIMD ALU Execute
32 FP32 FMA operations in parallel
8. Result Writeback
Route 32 results back through crossbar to register banks
Energy
0.3 pJ
0.6 pJ
0.3 pJ
0.5 pJ
0.8 pJ
0.4 pJ
0.7 pJ/op
0.3 pJ + 0.5 pJ
The operand collector exists because bank conflicts create variable latency.
It buffers partial results until ALL 32 thread operands are ready, then issues them as a unit into the SIMD engine.
This collector + the entire banked SRAM infrastructure is active on EVERY cycle, for EVERY warp instruction.
Why 64K registers? 2048 threads x 32 registers/thread = 65,536 registers. All threads must be resident to hide memory latency (100+ cycle HBM access).
The GPU cannot reduce the register file -- it IS the latency hiding mechanism. But powering 256 KB of banked SRAM every cycle is the energy cost of concurrency.

## Slide 4
GPU Energy Equation: Per-MAC Cost at the SM Level
Energy per CUDA Core MAC (amortized over 32-thread warp):
E_mac = (E_sched + E_scoreboard + E_addr_gen + E_bank_arb + E_sram_read + E_collector + E_crossbar) / 32 + E_alu + (E_result_route + E_sram_write) / 32
Simplified:
E_mac = E_overhead/32 + E_alu + E_writeback/32
"Concurrency Tax"
Useful Work
Result Delivery
Numerical Evaluation: CUDA Core Path at 4nm (H100-class)
Component | Per-Warp Energy (pJ) | Per-MAC (pJ) | Category | % of Total
Warp Scheduler | 0.50 | 0.016 | Control | 1.3%
Scoreboard Lookup | 0.30 | 0.009 | Control | 0.7%
Register Addr Gen (x3) | 0.60 | 0.019 | Operand Fetch | 1.5%
Bank Arbitration | 0.30 | 0.009 | Operand Fetch | 0.7%
SRAM Read (2 src) | 0.50 | 0.016 | Operand Fetch | 1.3%
Operand Collector | 0.80 | 0.025 | Operand Fetch | 2.0%
Crossbar Routing | 0.40 | 0.013 | Operand Fetch | 1.1%
CUDA Core ALU (FMA) | --- | 1.105 | Compute | 89.3%
Result Route + Write | 0.80 | 0.025 | Writeback | 2.0%
Total Energy per CUDA Core MAC at 4nm: 1.24 pJ
Ctrl: 0.025
Operand Fetch: 0.082
ALU: 1.105 pJ
WB: 0.025
Overhead: 11%
Useful Compute: 89%
CUDA cores: ALU dominates because overhead is amortized over 32 threads. But at the SM level, the banked SRAM + collectors draw continuous power.

## Slide 5
CPU vs GPU: Different Overhead, Same Stored-Program Problem
TensorCore Path (4x4x4 MMA = 64 MACs per instruction):
E_tc_mac = E_overhead/64 + E_tensor_alu + E_writeback/64 = ~1.65 pJ/MAC
TensorCores amortize overhead over 64 MACs (vs 32 for CUDA), reducing per-MAC overhead by 2x
Energy Breakdown Comparison at 4nm Process
Energy Component | CPU (scalar FP32) | GPU CUDA Core | GPU TensorCore
Instruction Frontend | 9.5 pJ (63%) | 0.025 pJ (2%) | 0.013 pJ (1%)
Operand Fetch / Delivery | 1.6 pJ (11%) | 0.082 pJ (7%) | 0.041 pJ (4%)
ALU / Compute | 1.8 pJ (12%) | 1.105 pJ (89%) | 0.34 pJ (29%)
Writeback | 0.9 pJ (6%) | 0.025 pJ (2%) | 0.010 pJ (1%)
Pipeline / Wire / Other | 1.2 pJ (8%) | --- | ---
TOTAL per operation | ~15.0 pJ | ~1.24 pJ | ~0.40 pJ
Overhead-to-ALU Ratio | 7.3x | 0.12x | 0.19x
But: The Full SM Picture -- Where the Energy Really Goes
Per-MAC numbers look great for the GPU. But the SM has:
* 64K registers (256 KB of banked SRAM) -- powered every cycle regardless of utilization
* 4 operand collectors -- continuously buffering, arbitrating, routing
* 4 warp schedulers + scoreboards -- tracking 64 warps of hazard state
* 32 register banks with crossbar -- always ready for next warp switch
This infrastructure exists to hide memory latency through thread concurrency.
At the SM level, the register file + operand delivery burns ~60% of compute power.
What if we could eliminate the register file entirely? (Next: Domain Flow Architecture)