## Slide 1
KPU Domain Flow Architecture:
Eliminating the Stored-Program Tax Entirely
The Stored-Program Problem:
CPU: Pays instruction tax on EVERY operation (fetch, decode, rename)
GPU: Amortizes instructions across 32 threads, but pays data movement tax
(64K registers, banked SRAM, operand collectors, crossbar routing)
The KPU Solution:
Eliminate BOTH taxes. No instruction fetch. No register file. No operand collectors.
Operands ARRIVE at the PE via compile-time-configured wire connections.
No Instruction Frontend
x No I-cache read
x No instruction decode
x No branch prediction
x No register rename
CPU: 9.5 pJ saved
No Register File Infra
x No 64K banked SRAM
x No operand collectors
x No bank arbitration
x No crossbar routing
GPU: ~3 pJ/warp saved
No Request/Reply Cycle
x No scoreboard lookup
x No address generation
x No result routing
x Compile-time scheduling
Both: 0 per-op overhead
Result: ~0.12 pJ per BF16 MAC vs GPU's ~1.65 pJ = 14x energy advantage per operation

## Slide 2
KPU Architecture: Programmable Spatial Dataflow
64 tiles x 256 PEs = 16,384 MACs/cycle -- executing Systems of Uniform Recurrence Equations (SURE)
Compute Fabric: 64 Programmable Tiles
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
16x16
Each tile: 16x16 PE array = 256 MACs/cycle | Programmable via SURE domain program
PE-to-PE connections: compile-time configured, wire-only transfer (~0.05 pJ)
EDDO Memory Hierarchy (Software-Managed)
DRAM (HBM2e / LPDDR5)
Off-chip | 10 pJ/byte | System bandwidth
DMA Engine
Bulk transfer | Double-buffered | 5 pJ setup/4KB
L3 Global Scratchpad (1-8 MB)
Distributed tiles | No tags | 2 pJ/byte | Compiler-managed
BlockMover Engine
L3 -> L2 block transfer | 0.8 pJ/byte routing
L2 Tile Staging (16-64 KB/tile)
Per-tile local | No coherence | 0.8 pJ/byte
Streamer Engine
Vector -> token stream | Token formation: 0.5 pJ
L1 Stream Buffers
Immediate fabric access | 0.3 pJ/byte
<-- feeds into --> Compute Fabric (SURE Network)
EDDO vs Hardware Caches: Why Software-Managed Memory Saves Energy
Hardware Cache (GPU/CPU):
Tag lookup on every access (~0.5 pJ)
Coherence protocol (GPU: ~5 pJ/request)
Reactive: fetch on miss, evict on full
Hardware decides placement at runtime
EDDO Scratchpad (KPU):
Direct addressing, no tag lookup (0 pJ)
No coherence protocol needed (0 pJ)
Proactive: compiler pre-stages ALL data
~50-60% energy of equivalent cache access

## Slide 3
The SURE Network: Operands Arrive, Not Fetched
Systems of Uniform Recurrence Equations define compile-time data routing between PEs
GPU: Request/Reply Cycle (per warp instruction)
1. Scoreboard Lookup
0.30 pJ
2. Register Addr Gen (x3)
0.60 pJ
3. Bank Arbitration
0.30 pJ
4. SRAM Read (32 banks)
0.50 pJ
5. Operand Collector
0.80 pJ
6. Crossbar Routing
0.40 pJ
7. ALU Execute
0.70 pJ/op
8. Result Route + Write
0.80 pJ
Total overhead per warp: 3.7 pJ | Per MAC: ~0.12 pJ overhead
KPU: Spatial Dataflow (per operation)
1. Operand arrives from neighbor PE (wire only)
0.05 pJ
2. ALU Execute (domain flow MAC, no fetch)
0.54 pJ
3. Result to local register (next PE's input, no arb)
0.02 pJ
Total per MAC: ~0.12 pJ overhead | 0.61 pJ total
What the SURE network eliminates:
x Scoreboard -- no hazards (compile-time schedule)
x Address generation -- no register addresses
x Bank arbitration -- no shared register file
x Operand collector -- no variable latency
x Crossbar routing -- direct PE-to-PE wires
x Result routing -- local register, no arbitration
The Physics: Why Wire Transfer is 50x Cheaper than Register File Access
PE-to-PE wire: ~0.05 pJ (0.1mm wire + 1 latch = C*V^2 for ~10fF capacitance)
GPU register: ~2.5 pJ (8KB SRAM bank + address decode + sense amplifier + bank arbitration + crossbar)
The wire is 50x cheaper because it is 100x shorter and has no address decode, no sense amplifier,
no arbitration, no tag comparison. This is not a design choice -- it is physics (Horowitz, ISSCC 2014).

## Slide 4
KPU Energy Equation: Per-MAC Cost at BF16
Energy per KPU Domain Flow MAC:
E_mac = E_pe_transfer + E_alu + E_local_write + E_config_amortized
Wire only (0.05 pJ)
Domain flow (0.54 pJ)
Local reg (0.02 pJ)
~0 (once/layer)
Numerical Evaluation: KPU-T768 at 7nm (Automotive-class)
Component | Per-Op Energy (pJ) | Category | % of Total | GPU Equivalent
PE-to-PE Transfer (x2 operands) | 0.044 | Data Movement | 3.9% | Scoreboard+Addr+Arb+Collector+Xbar: 2.9 pJ/warp
Domain Flow MAC (BF16) | 1.08 | Compute | 95.3% | TensorCore MAC: 0.34 pJ (similar)
Local Register Write | 0.009 | Data Movement | 0.8% | Result Route + RF Write: 0.8 pJ/warp
Accumulator (amortized) | 0.0945 | Compute | 8.3% | ---
Domain Config (amortized) | 0.0003 | Control | 0.0% | Kernel launch: 100K pJ (but 1-time)
TOTAL per BF16 MAC | 1.13 | ALL | 100% | GPU TensorCore: ~1.65 pJ/MAC
of which: overhead | 0.053 | Overhead | 4.7% | GPU overhead: ~0.12 pJ/MAC (amortized/64)
Energy per BF16 MAC at 7nm: 1.13 pJ -- 98% is useful compute
Data: 0.053
Compute: 1.17 pJ (96%)
GPU TensorCore for comparison: 1.65 pJ/MAC
Per-MAC overhead: 0.16
ALU: 0.34
SM infrastructure (RF, collectors, xbar): 1.15 pJ
Key Insight: The KPU spends 98% of energy on useful compute.
The GPU spends only 21% on useful compute -- the rest is operand delivery infrastructure
(register file, operand collectors, crossbar, scoreboard) that exists to support thread concurrency.
The KPU eliminates ALL of this by replacing request/reply with compile-time spatial routing.

## Slide 5
The Energy Efficiency Argument: CPU -> GPU -> TPU -> KPU
Each architectural step eliminates a class of overhead -- validated against Horowitz ISSCC 2014 scaling
 | CPU (Scalar FP32) | GPU CUDA Core | GPU TensorCore | TPU (Systolic) | KPU (Domain Flow)
Process Node | 7nm | 4nm | 4nm | 7nm | 7nm
Instruction Frontend | 9.5 pJ (63%) | 0.025 pJ | 0.013 pJ | ~0 pJ | ~0 pJ
Register File / RF | 1.6 pJ | 256 KB SRAM | 256 KB SRAM | PE registers | PE-local (1 reg)
Operand Delivery | RF read: 1.6 | Collector+Xbar | Collector | PE forwarding | Wire: 0.05 pJ
ALU / MAC Energy | 1.8 pJ | 1.1 pJ | 0.34 pJ | 0.14 pJ | 1.08 pJ (BF16)
Writeback | 0.9 pJ | 0.025 pJ | 0.010 pJ | PE-local | 0.009 pJ
Total per Operation | ~15 pJ | ~1.24 pJ | ~1.65 pJ* | ~0.8 pJ | ~1.13 pJ
Overhead/ALU Ratio | 7.3x | 0.12x | 0.19x | ~0.1x | ~0.05x
vs GPU TensorCore | 9x worse | 0.75x | 1.0x (base) | 2.1x better | 1.5x better
The System-Level 20x Energy Argument
Per-operation ALU energy is similar across architectures (~0.3-1.1 pJ at modern nodes).
The 20x advantage comes from THREE system-level factors:
1. Operand Delivery (5-10x): GPU pays 2.9 pJ/warp for scoreboard + collector + crossbar + arbitration.
KPU pays 0.05 pJ wire transfer. At the SM level, this infrastructure draws continuous power.
2. Memory Hierarchy (2-3x): GPU uses hardware caches with tag lookup + coherence protocol.
KPU uses EDDO scratchpads (no tags, no coherence) at 50-60% of cache energy.
3. Utilization (2-4x): GPU SM infrastructure (64K RF, 4 collectors) is always powered.
KPU tiles power-gate independently. Batch=1 utilization: KPU ~95% vs GPU ~30%.
Combined: 5-10x (operand delivery) x 2-3x (memory) x 2-4x (utilization) = 20-120x
* GPU TensorCore total includes SM-level infrastructure (register file, collectors) amortized across operations. Source: Horowitz ISSCC 2014 scaled to 4nm/7nm; validated against MLPerf MFU data.